## Slide 1: Embedded Software (bit-wise operators)
Fall, 2021

## Slide 2: Outline
Overview
Bit-wise operators
Bit manipulation
Programming exercises

## Slide 3: Overview
Bit manipulation is used to control the machine at low level
  Writing device drivers
  Pixel-level graphic programming
High-level programmer may not use this programing technique, but device driver programmer needs to handle this skillfully

## Slide 4
Hex and binary
  Hexadecimal is convenient way to represent binary
    0: 0000
    1: 0001
    9: 1001
    A: 1010
    F: 1111
  0xAF: 10101111
  0xBA: 10111010
  0x1AAF: 0001 1010 1010 1111

## Slide 5: Bit-wise operators
Bit-wise operators
Operator | Meaning
& | Bitwise AND
¦ | Bitwise OR
^ | Bitwise exclusive OR
~ | Complement
<< | Shift left
>> | Shift right

## Slide 6
Bitwise AND operator (&)
Bitwise OR operator ( | )
Bit1 | Bit2 | Bit1 & Bit2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Bit1 | Bit2 | Bit1 ¦ Bit2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7
Bitwise Exclusive OR (^)
Ones complement ( ~ )
Bit1 | Bit2 | Bit1 ^ Bit2
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Bit | ~Bit
0 | 1
1 | 0

## Slide 8
Left and right shift operator (<< , >>)
e.g.
 | c = 0x1C | 00011100
c << 1 | c = 0x38 | 00111000
c >> 2 | c = 0x07 | 00000111

## Slide 9
Bit values
Bit | Binary Value | Hex Constant
7 | 10000000 | 0x80
6 | 01000000 | 0x40
5 | 00100000 | 0x20
4 | 00010000 | 0x10
3 | 00001000 | 0x08
2 | 00000100 | 0x04
1 | 00000010 | 0x02
0 | 00000001 | 0x01

## Slide 10: Bit manipulation
An embedded processor interacts with a peripheral device through a set of control and status registers
  These registers are part of the peripheral hardware
Control and status registers are memory-mapped.
  Means that they can be handled just like ordinary pointer variables
  Each register has its own address

## Slide 11
Bitwise operators may be used to manipulate the contents of registers effectively;
if (*pTimerstatus & 0x08)
{
}
1> Testing the third bit;
2> Setting the forth bit;
*pTimerstatus |= 0x10;
int *pTimerstatus;
Bit | Binary Value | Hex
7 | 10000000 | 0x80
6 | 01000000 | 0x40
5 | 00100000 | 0x20
4 | 00010000 | 0x10
3 | 00001000 | 0x08
2 | 00000100 | 0x04
1 | 00000010 | 0x02
0 | 00000001 | 0x01

## Slide 12
*pTimerstatus &= ~(0x04)
3. Clearing the second bit;
4. Toggling the seventh bit;
*pTimerstatus ^= 0x80;
Bit | Binary Value | Hex
7 | 10000000 | 0x80
6 | 01000000 | 0x40
5 | 00100000 | 0x20
4 | 00010000 | 0x10
3 | 00001000 | 0x08
2 | 00000100 | 0x04
1 | 00000010 | 0x02
0 | 00000001 | 0x01

## Slide 13
Bitmask Macro
#define BIT(X) (1<<(X))
#define TIMER_STATUS BIT(5)
Bitmask:
a constant often used along with bitwise operators
e.g. #define TIMER_COMPLETE (0x80)
00100000
0x20
*pTimerstatus &= ~(0x20)
*pTimerstatus &= ~TIMER_STATUS

## Slide 14: Programming exercises (1)
7개의 LED를 갖는 LEDs 라는 unsigned char 변수에
  이진수 00000001을 대입하면, 0번째 LED 가 켜지고, 이진수 00000010 을 대입하면 1번째 LED 가 켜지고, … 이진수 1000000 을 대입하면 7번째 LED 가 켜지는 변수 LEDs 를 가정하자.
    unsigned char LEDs;
    LEDs=0x01;
    LEDs=0x02;
  0부터 7까지 숫자를 입력받아서, LEDs 값을 다음과 같이 바꾸어주는 함수를 작성하시오.
    int LED_function(int input);
    LED_function(2) 함수를 호출하면, 0x04 를 return 함
      LED_function 에서 16진수를 return 하거나, 이진수로 shift 연산자를 써서 return 함

## Slide 15
상기 프로그램을 어떻게 check 하나 ?
  int return_value;
  return_value=LED_function(2);
  printf(“return_value:%d\n”,return_value);
    4가 출력됨

## Slide 16: Programming exercises (2)
상기 프로그램을 활용하여,
  1. LEDs의 초기값을 이진수로 00000001을 대입하고,
  2. LEDs 값을 왼쪽으로 1만큼 계속 shift하고,
  3. LEDs 값이 이진수로 10000000 으로 대입되었을때
  4. 역으로 오른쪽으로 1만큼 계속 shift하는
  5. 과정이 총 4번 반복되는 프로그램을 작성하시오.
  정답은 ?
    출력 순서 ?
      1, 2, 4, 8,…, 128, 64 ….
    <반드시 shift 연산자를 사용할 것>

## Slide 17: Programming exercises (3)
Unsigned char 변수를 2진수로 변환하였을때, 1의 개수를 세고, 이를 다 왼쪽으로 shift 하였을때의 값을 출력하시오.
  Input: 01010110, 십진수: 86, 16진수: 0x56
  Output: 11110000, 십진수: 240, 16진수: 0xF0
  How to check?
    printf 문
    <정답> 위의 예의 출력 값은 ?
      1의 개수? 4
      Shift 시의 값은? 240
  scanf 함수를 사용해서 입력받도록 할 것
    scanf(“%uc”,&LEDs);

## Slide 18: Programming exercises (4)
시간이 남으면, 추가로 자유롭게 bit manipulation 프로그램을 작성해 볼 것